## Slide 1
  CNTT - Edge WS
  Use Cases Assessment

## Slide 2: Telco Edge Basic Characterstics Vs Edge Use Cases
Commonly coupled with 5G. Seen as one of the ingredients of the ultra-low latency/eMBB Network Slice.
Requirements for user plane Local Breakout / Termination. This requires that VASs, CDN, & Any Gi-LAN applications are locally hosted at the Edge.
Current focus is to provide PaaS for Operator’s application while having a real platform allowing 3rd party Applications in roadmaps.
Perfect fit for vRAN vDU/vCU placements preserving the latency requirements.
UPF
Edge NFVI
CU
DU
VASs
CDN
Analytics
App (IoT)
App (V2X)
3rd Party APP
App (VR)
Telco Edge Environment
Traffic Steering / SFC
CU
DU
RU
IaaS
PaaS
28 SST
224 SD
4 stand. SST
Notes: Besides requiring low-latency, high-bandwidth, and high reliability, newly generated edge computing services require the local deployment environment to be capable of doing fast computing to support some intelligence functions like real-time data analysis and optimal path calculation of services like V2X. The deployment of MEC and third-party applications running on it mainly depends on latency requirements. uRLLC requires E2E delay less than 3ms, which means it should be deployed at edge sites close to base station. eMBB requires E2E delay less than 10ms, which leads to more flexible deployment location.

## Slide 3: Telco Edge Basic Characterstics Vs Edge Use Cases
Edge Network Slice
UPF
Edge NFVI
CU
DU
VASs
CDN
Analytics
App (IoT)
App (V2X)
3rd Party APP
App (VR)
Telco Edge Environment
Traffic Steering / SFC
CU
DU
RU
IaaS
PaaS
Standard 3GPP Network Slice
Part of
Commercial
Custom Slices
Part of Commercial Custom Slices

## Slide 4: Edge Use Cases – Current Focus
UPF
Edge NFVI
CU
DU
VASs
CDN
Analytics
App (IoT)
App (V2X)
3rd Party APP
App (VR)
Telco Edge Environment
Traffic Steering / SFC
CU
DU
RU
IaaS
PaaS
vRAN
Edge Slice + VAS/App (eMBB)
Edge Slice + VAS/App (uRLLC)
Edge Slice + VAS/App (IoT)

## Slide 5: Use Cases proposal for Telco Edge
vRAN Use Case //Quick Win //OpenRAN (TIP) Potential Cooperation
Edge Network Slicing – UPF (Private 5G/Virtual Campus) //Trending use case //VNF/CNF
Edge Network Slicing with CDN //Perfect fit for the eMBB Slice use case
Edge Automotive use case (V2X) //Perfect fit for the uRLLC Slice use case
Remote Surveillance with Video Analytics //Perfect fit for the mission critical (IoT) Slice use case

## Slide 6: Use Case Screening
Edge Network Slicing with CDN
UPF
Edge NFVI
Telco Edge Environment
CU
DU
RU
IaaS
PaaS
CDN
Network
Slice
Traffic Steering

## Slide 7: Use Case Screening
Edge Network Slicing for Private 5G (Virtual Campus Network)
UPF
Cloud Infrastructure (NFVI)
Telco Edge Environment (Customer Premises)
CU
DU
RU
Private 5G Network
Slice
Customer Premises
Traffic Steering / SFC
App
1
App
2
AppN

## Slide 8: Use Case Screening
Edge Network Slicing for V2X (V2N - Remote Driving)
UPF
Cloud Infrastructure (NFVI)
Telco Edge Environment
CU
DU
RU
5G V2X Network Slice
V2X AS
Road Transport Authorities
Automotive X
AS

## Slide 9: Use Case Screening
vRAN
UPF
Edge NFVI
CU
DU
VASs
CDN
Analytics
App (IoT)
App (V2X)
3rd Party APP
App (VR)
Telco Edge Environment
Traffic Steering / SFC
RU
vRAN

## Slide 10: Openstack – Edge Computing Group
Mobile Service Provider 5G/4G virtual RAN deployment & Edge Cloud B2B2X (Needs Some Updates)
uCPE for Enterprise Network Services
Unmanned Aircraft System (Drones)
Cloud Storage Gateway (Storage at the Edge)
Open Caching – Stream/Store Data at the Edge
Smart City as Software Defined Closed-loop system
Augmented Reality – Sony Gaming Network
Analytics/Control at the Edge
Manage Retail Chain – Chich-fil-a
Smart Home
Data Collection – Smart Cooler/cold chain tracking
VPN Gateway service Delivery
Additional use cases
(Remote Surveillance, Unmanned Aerial System (Drones), Compliance Requirements, NFV, Respect Data Privacy, Industrial Control / Factory Automation, 5G Service Delivery over non-IP SDN-based Core, Automotive Edge Computing, Data Collection & Analytics, Real time, Immersive, Network Efficiency)

## Slide 11: OPNFV – Telco Edge Use Cases
CRAN-CU
UPF, SAE-GW
Enterprise CPE
Edge CDN
MEC/Edge Computing Service (Not clearly explained)
Note- It seems that the exercise was not completed.