## Slide 1: CREATING A COMMON TELCO NFVi
Artifacts

## Slide 2
Bogo-Meter | On front of each chapter.
Bogo-Meter rating
Complete
Dickering over the fine points
Lots of SME feedback
Still developing content
Initial framework only

## Slide 3
Reference NFVI Hardware
Reference NFVI Software
Infrastructure Profiles Catalogue
Compliance & Certification, and Verification
NFVI Metrics & Capabilities
VNF Requirements
VNF
VNF
VNF
VNF
N
C
B
Infrastructure Abstraction
NFVI Metrics & capabilities
Infrastructure Profiles Catalogue
Infrastructure Profiling
Reference NFVI SW/HW Profiles and configurations
----
CNTT | Scope.

## Slide 4
Basic
OFCS
Compute Intensive
Example VNFs
Example VNFs
Predictable computing
-
Low latency networking
CNTT | Profiles.
Network Intensive
Example VNFs
Predictable computing
-
Low latency & high throughput networking
Standard computing
NMS
AAA
MME
CSCF
AMF
BNG
DPI
PGW

## Slide 5
VNF
Instance A
Compute Flavours
Metrics & Capabilities
S
M
L
Metric | Value
Instance B
Compute Flavours
Metrics & Capabilities
S
M
L
Metric | Value
Instance C
Compute Flavours
Metrics & Capabilities
S
M
L
Metric | Value
VNF
VNF
VNF
VNF-C
N
VNF-C
B
VNF-C
B
VNF-C
B
VNF-C
B
VNF-C
H
VNF-C
N
VNF-C
B
…
…
…
…
CNTT | VNF Construct.

## Slide 6
VNF
Control
VNF-C
DP
VNF-C
DP
VNF-C
S
B
M
N
L
N
Instance type
Compute flavour
CNTT | VNF Construct.

## Slide 7
crypto look-aside
.la-crypto
ipsec in-line
.il-ipsec
transcoding look-aside
.la-trans
Network Acceleration (A extension)
S extensions (Ext. Storage)
.100GB
default storage type
.200GB
default storage type
.300GB
default storage type
.blk100GB
block storage type
.blk200GB
block storage type
.blk300GB
block storage type
Compute Flavours
.tiny
1 vCPU
512MB RAM
.small
1 vCPU
2 GB RAM
.medium
2 vCPU
4GB RAM
.large2
4 vCPU
16GB RAM
.xlarge
8 vCPU
16GB RAM
.xlarge2
8 vCPU
32GB RAM
.large
4 vCPU
8GB RAM
.xlarge3
8 vCPU
64GB RAM
1 GB Disk
40 GB Disk
40 GB Disk
80 GB Disk
80 GB Disk
160 GB Disk
160 GB Disk
160 GB Disk
1 Gbps
1 Gbps
1 Gbps
1 Gbps
1 Gbps
1 Gbps
1 Gbps
1 Gbps
B Instance Basic
(I) Interfaces Options
B <I opt> . <flavour> . <S ext>
Can be instantiated in any Data Centre.
1
1x 1Gbps
10
1x 10Gbps
1D
2x 1Gbps
10D
2x 10Gbps
1T
3x 1Gbps
10T
3x 10Gbps
…
…
N Instance Network intensive
(I) Interfaces Options
N <I opt> . <flavour> . <S ext> . <A ext>
Aimed for regional data centres, Access, & POP.
25
1x 25Gbps
40D
2x 40Gbps
25D
2x 25Gbps
100
1x 100Gbps
40
1x 40Gbps
100D
2x 100Gbps
…
…
H Instance Compute intensive
(I) Interfaces Options
H <I opt> . <flavour> . <S ext> . <A ext>
Aimed for local data centres, and on Edge.
25
1x 25Gbps
40D
2x 40Gbps
25D
2x 50Gbps
50
1x 50Gbps
40
1x 40Gbps
50D
2x 50Gbps
…
…
Programmable look-aside
.la-prog
Compute Acceleration (A extension)
CNTT | Catalogue.

## Slide 8
NFVI SW Infrastructure (NFVI)
Virtual Networking
VNF
VNF-C
VNF-C
vPort
…
vPort
VNF-C
vPort
…
vPort
vPort
…
vPort
vNIC interface
e.g. virt-io
Compute nodes
VIM (Virtual Infrastructure Management)
Control nodes
Virtual Storage
Virtual Compute
SDN
CNTT | Basic SW Config.

## Slide 9
NFVI SW Infrastructure (NFVI)
Accelerated/Offloaded Virtual Networking
VNF
VNF-C
VNF-C
vPort
…
vPort
vPort
…
vPort
vPort
…
vPort
vNIC interface
e.g. virt-io
Compute nodes
VIM (Virtual Infrastructure Management)
Control nodes
Virtual Storage
Virtual Compute
SDN
Network Accelerators
Acc interface
e.g. virtio-ipsec
VNF-C
CNTT | NI SW Config.

## Slide 10
NFVI SW Infrastructure (NFVI)
Accelerated Virtual Networking
VNF
VNF-C
VNF-C
vPort
…
vPort
vPort
…
vPort
vPort
…
vPort
vNIC interface
e.g. virt-io
Compute nodes
VIM (Virtual Infrastructure Management)
Control nodes
Virtual Storage
Virtual Compute
SDN
HW Accelerators FPGA/CPU/NPU
HW Acc interface
VNF-C
CNTT | CI SW Config.

## Slide 11
Basic
Virtual Compute, Network, and Storage
Over-subscription
HA
Network Intensive
SDN controller
CPU Pinning
Virtual Compute, Network, Acceleration, and Storage
Zero over-subscription
HA
Compute Intensive
Monitoring
NVMe/SSD
Virtual Compute, Network, GPU/FPGA, and Storage
Zero over-subscription
HA
Basic
2 x16-core @ 2.2 GHz
256 GB RAM
2 x 10 GbE
HDD
SSD
Network Intensive
2 x 20-core @ 2.1 GHz
SmartNIC / HW Acceleration
512 GB RAM
2 x 25GbE
HDD
SSD
Compute Intensive
2 x 24-core @ 2.1 GHz
FPGA / GPU / HW Acceleration
768GB RAM
2 x 25GbE
HDD
SSD
CNTT | HW/SW Config.

## Slide 12
CNTT | HW/SW Config.
Basic
SMT/HT
PCIe
#NIC
SSD
#CPU
#Cores
RAM(GB)
HDD
Network Intensive
SMT/HT
PCIe
#NIC
SSD
#CPU
#Cores
RAM(GB)
HDD
Network Acc
HW Offloads
Compute Intensive
SMT/HT
PCIe
#NIC
SSD
#CPU
#Cores
RAM(GB)
HDD
FPGA/GPU
HW Offloads

## Slide 13
Memory
Memory
CPU 1
CPU 0
CNTT | Basic HW Config.

## Slide 14
Memory
Memory
CPU 1
CPU 0
HW offload
HW offload
Internal/External
Hardware Acceleration
CNTT | NI HW Config.

## Slide 15
Memory
Memory
CPU 1
CPU 0
Internal/External
Hardware Acceleration
CNTT | CI HW Config.

## Slide 16: Diagram based on Terminology
VNF on VM
VNF on Container on VM
VNF on Container
Containers
_________
Container Runtime + Networking
Containers
______________
Container Runtime + Networking
Hypervisor (KVM, ESXi)
VM
VM
Virtual
Network
Neutron
NSX
Virtual
Network
Contrail

## Slide 17: Software Terminologies
vApp
VNF
CNF
VM
Hypervisor
NFVI SW Layer
Network Function
Network Service
Service Layer
Application Layer
Container
workload
Compute | Networks | Storage
Virtual Resources
Container Engine
NFVI SW Configuration
NFVI SW Profile
VM Instances
Catalogue
Instance Type
Compute flavour

## Slide 18: Hardware Layers Terminologies
NFVI HW Layer
Compute | Networks | Storage
Hardware Resources
NFVI HW Configuration
NFVI HW Profile
Compute
Storage
Network
Physical
Network Function
(PNF)

## Slide 19
Desired State
Attribute1: value1
Attribute2: value2
Attribute3: value3
Observed State
Attribute1: value1
Attribute2: value2
Attribute3: value4
Infrastructure / Infrastructure Management
Configuration Management System
1
2
3
4
5

## Slide 20: Thank you