## Slide 1: CREATING A COMMON TELCO NFVi
Artifacts

## Slide 2
Bogo-Meter | On front of each chapter.
Bogo-Meter rating
Complete
Dickering over the fine points
Lots of SME feedback
Still developing content
Initial framework only

## Slide 3
Reference NFVI Hardware
Reference NFVI Software
Infrastructure Profiles Catalogue
Compliance & Certification, and Verification
NFVI Metrics & Capabilities
VNF Requirements
VNF
VNF
VNF
VNF
N
C
B
Infrastructure Abstraction
NFVI Metrics & capabilities
Infrastructure Profiles Catalogue
Infrastructure Profiling
Reference NFVI SW/HW Profiles and configurations
----
CNTT | Scope.

## Slide 4
Basic
OFCS
Compute Intensive
Example workload
Example VNFs
Predictable computing
-
Low latency networking
CNTT | Profiles.
Network Intensive
Example workload
Predictable computing
-
Low latency & high throughput networking
Standard computing
NMS
AAA
MME
CSCF
AMF
BNG
DPI
PGW

## Slide 5
Edge
Network Intensive
Basic
OFCS
Example workload
CNTT | Profiles.
Predictable computing
-
Low latency & high throughput networking
Standard computing
Example Workload
Very Low latency networking
Use case driven profile &
Special Tech required
AAA
NMS
BNG
PGW
DPI
Example workload
vDU
AL/ML
Gaming
CDN
GiLAN

## Slide 6
VNF
Instance A
Compute Flavours
Metrics & Capabilities
S
M
L
Metric | Value
Instance B
Compute Flavours
Metrics & Capabilities
S
M
L
Metric | Value
Instance C
Compute Flavours
Metrics & Capabilities
S
M
L
Metric | Value
VNF
VNF
VNF
VNF-C
N
VNF-C
B
VNF-C
B
VNF-C
B
VNF-C
B
VNF-C
H
VNF-C
N
VNF-C
B
…
…
…
…
CNTT | VNF Construct.

## Slide 7
CNTT | NFVI Model Overview (Figure 3-1)
Cloud Infrastructure
Physical resources
Virtual resources
Management software
VNFs/CNFs
Management client
Consumes virtual resources
Manages virtual resources

## Slide 8
CNTT | NFVI Model Overview (Figure 3-2)
Cloud Infrastructure
Physical resources
Virtual resources
Management software
VNFs/CNFs
Management client
Consumes virtual resources
Manages virtual resources
Virtual resources
Tenant
Network
Compute
Storage
Belongs to
Belongs to
Belongs to
Connected to
Attaches

## Slide 9
CNTT | NFVI Management Software (Figure 3-3)
Cloud Infrastructure
Physical resources
Virtual resources
Management software
VNFs/CNFs
Management client
Consumes virtual resources
Manages virtual resources
Management software
Network resources manager
Compute resources manager
Storage resources manager
Catalog
Inventory
Scheduler
Monitoring
Additional management functions
API / user interface

## Slide 10
CNTT | NFVI Physical Resources (Figure 3-4)
Cloud Infrastructure
Physical resources
Virtual resources
Management software
VNFs/CNFs
Management client
Consumes virtual resources
Manages virtual resources
Physical resources
Network
Compute
Storage

## Slide 11
CNTT | VNF Construct (Figure 4-1)
Cloud Infrastructure
Cloud Infrastructure hardware and software profile
Virtual infrastructure resources
Workloads
Consumes infrastructure resources
Manages infrastructure via API-s
Exposed objects are visible in the workload and in the cloud infra management domain.
Internal objects are exclusively visible only in the Cloud Infrastructure and Cloud Infrastructure management domains.

## Slide 12
Workload
Control
VM or Pod
DP
VM or Pod
DP
VM or Pod
B
N
N
CNTT | VNF Construct (Figure 4-2).
S
L
M
Cloud Infrastructure Profile
Compute flavour

## Slide 13
CNTT | Cloud Infrastructure software layers (Figure 5-1)
Cloud Infrastructure Software Profile
Host Operating System
Virtualisation Infrastructure Layer (Hypervisor or container based virtualization technology)

## Slide 14
Cloud Infrastructure
Virtual Networking
Workload
VM or Pod
VM or Pod
interface
…
interface
VM or Pod
interface
…
interface
interface
…
interface
Virtual interface
e.g. virt-io
Compute nodes
Cloud Infrastructure Management
Control nodes
Virtual Storage
Virtual Compute
SDN
CNTT | Cloud Infrastructure Virtual resources (Figure 5-2)

## Slide 15
CNTT | (Figure 9-1)
Computing
Hardware
Storage
Hardware
Network
Hardware
Hardware resources
Virtualisation Layer
VNF
Manager(s)
VNF 2
NFV Orchestrator
OSS/BSS
NFVI
VNF 3
VNF 1
Execution reference points
Main NFV reference points
Other reference points
Virtual Computing
Virtual Storage
Virtual Network
EMS 2
EMS 3
EMS 1
Service, VNF and Infrastructure Description
Or-Vi
Or-Vnfm
Vi-Vnfm
Os-Ma
Se-Ma
Ve-Vnfm
Nf-Vi
Vn-Nf
Vl-Ha
Virtualized Infrastructure Manager(s)
Reference Model scope
API and interfaces
Infrastructure abstraction
Cloud Infrastructure Software
Cloud Infrastructure Hardware

## Slide 16
crypto look-aside
.la-crypto
ipsec in-line
.il-ipsec
transcoding look-aside
.la-trans
Network Acceleration (A extension)
S extensions (Ext. Storage)
.100GB
default storage type
.200GB
default storage type
.300GB
default storage type
.blk100GB
block storage type
.blk200GB
block storage type
.blk300GB
block storage type
Compute Flavours
.tiny
1 vCPU
512MB RAM
.small
1 vCPU
2 GB RAM
.medium
2 vCPU
4GB RAM
.large2
4 vCPU
16GB RAM
.xlarge
8 vCPU
16GB RAM
.xlarge2
8 vCPU
32GB RAM
.large
4 vCPU
8GB RAM
.xlarge3
8 vCPU
64GB RAM
1 GB Disk
40 GB Disk
40 GB Disk
80 GB Disk
80 GB Disk
160 GB Disk
160 GB Disk
160 GB Disk
1 Gbps
1 Gbps
1 Gbps
1 Gbps
1 Gbps
1 Gbps
1 Gbps
1 Gbps
B Instance Basic
(I) Interfaces Options
B <I opt> . <flavour> . <S ext>
Can be instantiated in any Data Centre.
1
1x 1Gbps
10
1x 10Gbps
1D
2x 1Gbps
10D
2x 10Gbps
1T
3x 1Gbps
10T
3x 10Gbps
…
…
N Instance Network intensive
(I) Interfaces Options
N <I opt> . <flavour> . <S ext> . <A ext>
Aimed for regional data centres, Access, & POP.
25
1x 25Gbps
40D
2x 40Gbps
25D
2x 25Gbps
100
1x 100Gbps
40
1x 40Gbps
100D
2x 100Gbps
…
…
H Instance Compute intensive
(I) Interfaces Options
H <I opt> . <flavour> . <S ext> . <A ext>
Aimed for local data centres, and on Edge.
25
1x 25Gbps
40D
2x 40Gbps
25D
2x 50Gbps
50
1x 50Gbps
40
1x 40Gbps
50D
2x 50Gbps
…
…
Programmable look-aside
.la-prog
Compute Acceleration (A extension)
CNTT | Catalogue.

## Slide 17
crypto look-aside
.la-crypto
ipsec in-line
.il-ipsec
Network Acceleration (A extension)
S extensions (Ext. Storage)
.bronze
Up to 3k(R), 1.5K(W) IOPS
.silver
Up to 60k(R), 30K(W) IOPS
.gold
Up to 680k(R), 360K(W) IOPS
Compute Flavours
.tiny
1 vCPU
512MB RAM
.small
1 vCPU
2 GB RAM
.medium
2 vCPU
4GB RAM
1 GB Disk
20 GB Disk
40 GB Disk
1 Gbps
1 Gbps
1 Gbps
.large
4 vCPU
8GB RAM
80 GB Disk
1 Gbps
.2xlarge
8 vCPU
16GB RAM
.4xlarge
16 vCPU
32GB RAM
160 GB Disk
320 GB Disk
1 Gbps
1 Gbps
Basic Profile
(I) Interfaces Options
B <I opt> . <flavour> . <S ext>
Can be instantiated in any Data Centre.
1
N x 1Gbps
50
Nx 50Gbps
10
N x 10Gbps
100
N x 100Gbps
25
N x 25Gbps
Network Intensive Profile
(I) Interfaces Options
N <I opt> . <flavour> . <S ext> . <A ext>
Aimed for regional data centres, Access, & POP.
1
N x 1Gbps
50
N x 50Gbps
10
N x 10Gbps
100
N x 100Gbps
25
Nx 25Gbps
CNTT | Catalogue.

## Slide 18
NFVI SW Infrastructure (NFVI)
Virtual Networking
VNF
VNF-C
VNF-C
vPort
…
vPort
VNF-C
vPort
…
vPort
vPort
…
vPort
vNIC interface
e.g. virt-io
Compute nodes
VIM (Virtual Infrastructure Management)
Control nodes
Virtual Storage
Virtual Compute
SDN
CNTT | Basic SW Config.

## Slide 19
NFVI SW Infrastructure (NFVI)
Accelerated/Offloaded Virtual Networking
VNF
VNF-C
VNF-C
vPort
…
vPort
vPort
…
vPort
vPort
…
vPort
vNIC interface
e.g. virt-io
Compute nodes
VIM (Virtual Infrastructure Management)
Control nodes
Virtual Storage
Virtual Compute
SDN
Network Accelerators
Acc interface
e.g. virtio-ipsec
VNF-C
CNTT | NI SW Config.

## Slide 20
NFVI SW Infrastructure (NFVI)
Accelerated Virtual Networking
VNF
VNF-C
VNF-C
vPort
…
vPort
vPort
…
vPort
vPort
…
vPort
vNIC interface
e.g. virt-io
Compute nodes
VIM (Virtual Infrastructure Management)
Control nodes
Virtual Storage
Virtual Compute
SDN
HW Accelerators FPGA/CPU/NPU
HW Acc interface
VNF-C
CNTT | CI SW Config.

## Slide 21
Basic
Virtual Compute, Network, and Storage
Over-subscription
HA
Network Intensive
SDN controller
CPU Pinning
Virtual Compute, Network, Acceleration, and Storage
Zero over-subscription
HA
Compute Intensive
Monitoring
NVMe/SSD
Virtual Compute, Network, GPU/FPGA, and Storage
Zero over-subscription
HA
Basic
2 x16-core @ 2.2 GHz
256 GB RAM
2 x 10 GbE
HDD
SSD
Network Intensive
2 x 20-core @ 2.1 GHz
SmartNIC / HW Acceleration
512 GB RAM
2 x 25GbE
HDD
SSD
Compute Intensive
2 x 24-core @ 2.1 GHz
FPGA / GPU / HW Acceleration
768GB RAM
2 x 25GbE
HDD
SSD
CNTT | HW/SW Config.

## Slide 22
Basic
Storage with Encryption
vCPU Over-subscription
Compute Intensive
Monitoring
NVMe/SSD
Virtual Compute, Network, GPU/FPGA, and Storage
Zero over-subscription
HA
Basic
2 x16-core @ 2.2 GHz
256 GB RAM
2 x 10 GbE
HDD
SSD
Network Intensive
2 x 20-core @ 2.1 GHz
SmartNIC / HW Acceleration
512 GB RAM
2 x 25GbE
HDD
SSD
Compute Intensive
2 x 24-core @ 2.1 GHz
FPGA / GPU / HW Acceleration
768GB RAM
2 x 25GbE
HDD
SSD
CNTT | HW/SW Config.
Network Intensive
Huge Pages
CPU Pinning
Network Acceleration
Storage with Encryption and Replication
No vCPU Over-subscription

## Slide 23
CNTT | HW/SW Config.
Basic
SMT/HT
#NIC
HDD/SSD
#CPU
#Cores
RAM
Network Intensive
SMT/HT
PCIe
#NIC
SSD
#CPU
#Cores
RAM(GB)
HDD
Network Acc
HW Offloads
Compute Intensive
SMT/HT
PCIe
#NIC
SSD
#CPU
#Cores
RAM(GB)
HDD
FPGA/GPU
HW Offloads
Basic
SMT/HT
PCIe
#NIC
SSD
#CPU
#Cores
RAM(GB)
HDD
Network Intensive
SMT/HT
#NIC
HDD/SSD
#CPU
#Cores
RAM
NUMA
HW Offloads
(e.g. SmartNIC)

## Slide 24
Memory
Memory
CPU 1
CPU 0
CNTT | Basic HW Config.

## Slide 25
Memory
Memory
CPU 1
CPU 0
HW offload
HW offload
Internal/External
Hardware Acceleration
CNTT | NI HW Config.

## Slide 26
Memory
Memory
CPU 1
CPU 0
Internal/External
Hardware Acceleration
CNTT | CI HW Config.

## Slide 27: Diagram based on Terminology
VNF on VM
VNF on Container on VM
VNF on Container
Containers
_________
Container Runtime + Networking
Containers
______________
Container Runtime + Networking
Hypervisor (KVM, ESXi)
VM
VM
Virtual
Network
Neutron
NSX
Virtual
Network
Contrail

## Slide 28: Software Terminologies
vApp
VNF
CNF
VM
Hypervisor
NFVI SW Layer
Network Function
Network Service
Service Layer
Application Layer
Container
workload
Compute | Networks | Storage
Virtual Resources
Container Engine
NFVI SW Configuration
NFVI SW Profile
VM Instances
Catalogue
Instance Type
Compute flavour

## Slide 29: Hardware Layers Terminologies
NFVI HW Layer
Compute | Networks | Storage
Hardware Resources
NFVI HW Configuration
NFVI HW Profile
Compute
Storage
Network
Physical
Network Function
(PNF)

## Slide 30
Desired State
Attribute1: value1
Attribute2: value2
Attribute3: value3
Observed State
Attribute1: value1
Attribute2: value2
Attribute3: value4
Infrastructure / Infrastructure Management
Configuration Management System
1
2
3
4
5

## Slide 31
OVS-Kernel
Compute
NIC0
NIC1
NIC3
NIC2
NIC4
Internal API
Storage Management
Ceph
Storage
NIC0
NIC1
NIC3
NIC2
NIC4
Controller
NIC0
NIC1
NIC3
NIC2
NIC4
Foundation
NIC0
NIC1
Provisioning & Management
Storage Front-end
Tenant
External API
External Provider (FIP)
Bond
Bond
Bond
Bond
Bond
Bond
OVS-DPDK
Compute
NIC0
NIC1
NIC2
NIC3
NIC4
Bond
Bond
NUMA 0
NUMA 1
IPMI
IPMI
IPMI
IPMI
IPMI
External Provider (VLANs)
IPMI / Out of band
Key
802.1q tagged Native

## Slide 32
Deployment node(s)
Host OS + Hardware Drivers
API endpoints
Control nodes
Compute nodes
Dashboard
HORIZON
Orchestration
HEAT
Compute
NOVA
Block
Storage
CINDER
Networking
NEUTRON
Tenant Services
KEYSTONE
OS Image
Repository
GLANCE
Cloud Deployment (Foundation)
\
Object
Storage
SWIFT or compatible
BMaaS
Optional
Common Services for OpenStack (databases, messaging, etc.)
Compute
NOVA
Networking
NEUTRON
Monitoring
Alerting
Qemu/KVM
Hypervisor
Virtual switch
OvS / DPDK
Monitoring
Alerting
Logging, monitoring and alerting node(s)
Logging
Monitoring
Alerting
Storage nodes
Shared Storage
Host OS + Hardware Drivers
vRouter
vR / DPDK

## Slide 33
Compute Nodes
Physical Infrastructure Resources
Operating System Kernel
Underlay Network
Container Orchestration
Kubernetes / Kubelet
Container Runtime
Container Networking
CNI
Libvirt/KVM
Nova-compute , Neutron-agent
libvirt exec space
Project (Tenant) A
VM
VM
Project (Tenant) B
VM
VM
Control Nodes
Storage
CSI / SDS
Containerized OpenStack Services
Keystone, Glance, Nova, Neutron, Cinder, Swift
Physical Infrastructure Resources
Operating System Kernel
Underlay Network
Container Orchestration
Kubernetes / Kubelet
Container Runtime
Container Networking
CNI
Figure 4-2: Containerised OpenStack Services Topology

## Slide 34
● ● ● ● ● ● ● ●
● ● ● ● ● ● ● ●
● ● ● ● ● ● ● ●
● ● ● ● ● ● ● ●
● ● ● ● ● ● ● ●
● ● ● ● ● ● ● ●
● ● ● ● ● ● ● ●
● ● ● ● ● ● ● ●
● ● ● ● ● ● ● ●
● ● ● ● ● ● ● ●
● ● ● ● ● ● ● ●
● ● ● ● ● ● ● ●
● ● ● ● ● ● ● ●
● ● ● ● ● ● ● ●
● ● ● ● ● ● ● ●
● ● ● ● ● ● ● ●
● ● ● ● ● ● ● ●
● ● ● ● ● ● ● ●
● ● ● ● ● ● ● ●
● ● ● ● ● ● ● ●
● ● ● ● ● ● ● ●
● ● ● ● ● ● ● ●
● ● ● ● ● ● ● ●
● ● ● ● ● ● ● ●
● ● ● ● ● ● ● ●
● ● ● ● ● ● ● ●
● ● ● ● ● ● ● ●
● ● ● ● ● ● ● ●
● ● ● ● ● ● ● ●
● ● ● ● ● ● ● ●
● ● ● ● ● ● ● ●
● ● ● ● ● ● ● ●
● ● ● ● ● ● ● ●
● ● ● ● ● ● ● ●
● ● ● ● ● ● ● ●
● ● ● ● ● ● ● ●
● ● ● ● ● ● ● ●
● ● ● ● ● ● ● ●
● ● ● ● ● ● ● ●
● ● ● ● ● ● ● ●
● ● ● ● ● ● ● ●
● ● ● ● ● ● ● ●
● ● ● ● ● ● ● ●
● ● ● ● ● ● ● ●
● ● ● ● ● ● ● ●
● ● ● ● ● ● ● ●
● ● ● ● ● ● ● ●
● ● ● ● ● ● ● ●
● ● ● ● ● ● ● ●
● ● ● ● ● ● ● ●
● ● ● ● ● ● ● ●
● ● ● ● ● ● ● ●
● ● ● ● ● ● ● ●
● ● ● ● ● ● ● ●
● ● ● ● ● ● ● ●
● ● ● ● ● ● ● ●
● ● ● ● ● ● ● ●
● ● ● ● ● ● ● ●
● ● ● ● ● ● ● ●
● ● ● ● ● ● ● ●
TOR Switch A
TOR Switch A
TOR Switch A
TOR Switch B
TOR Switch B
TOR Switch B
Spine Switch 1
Spine Switch 2
Spine Switch n
Servers
● ● ●
● ● ●
Rack 1
Rack 2
Rack n

## Slide 35
HW Layer (hwmon)
Operating System Layer
OpenStack Services
Non OpenStack Services
Fluentd Aggregator POD
Prometheus
(monitoring)
Alerting
Elasticsearch
Kibana
(Visualisataion)
Log metrics
Log/events
DB
PVC
Controller Node
OpenStack (nova-compute, libvirt, …)
Operating System Layer
HW Layer (hwmon)
Non OpenStack Services
Controller Node(s)
Compute Node(s)

## Slide 36
Reference Model v3.0
Figure-1 : CNTT Stable 3.0 Portrait
Apr 2020
RM Baldy
Sep 2020
Apr 2021
Sep 2021
Reference Architecture-1 v3.0
Reference Implementation-1 v3.0
Reference Architecture-2 v3.0
Reference Implementation-2 v3.0
Reference Conformance-1 v3.0
Reference Conformance-2 v3.0
V3.0 Stable
Release Timeline
Fed into RA2
Fed into RA1
RM Baldy
RA2 Baraque
Fed into RI2
RA1 Baraque
Fed into RI1
RA2 of Next Rel
Fed into RC2
RI1 of Next Rel
Fed into RC1
Baldy | Baraque | TBD | TBD
RM v3.0 | RM v4.0 | RM v5.0 | RM v6.0
RA v2.0 | RA v3.0 | RA v4.0 | RA v5.0
RI v1.0 | RI v2.0 | RI v3.0 | RI v4.0
Not Started | RC v1.0 | RC v2.0 | RC v3.0
Quick Reference – Evolving in each release

## Slide 37: Thank you